## Slide 1: Routing Decision in SDN: Performance of Reactive Flow Installation in Max-min Fair Network
EL 7363 Final Project
Kuan-yin Chen, Soheil Abbasloo
Spring 2015
NYU

## Slide 2: Today: ECMP Load Balancing
Traditional Load Balancing schemes like ECMP are Local-Aware
  No Global Sense of the bottlenecks in the network
  Local-awareness makes them sub optimal solutions for Max-Min fairness

## Slide 3: Local Load Balance Schemes
40G
40G
40G
40G
40G
Schemes using local knowledge are sub optimal
10
10 flows
20 flows

## Slide 4: Local Load Balance Schemes
40G
40G
40G
40G
40G
10
10
10
10 flows
20 flows
Schemes using local knowledge are sub optimal
20

## Slide 5: What about a Global-Aware Scheme?

## Slide 6: Global-Aware Scheme
40G
40G
40G
40G
40G
10
5
15
10 flows
20 flows
Global knowledge leads to better solution!
15
So Lets Use Global-Awareness.
But How?

## Slide 7: Global-Awareness?
Software Defined Network (SDN)
  Monitor whole of the Network in a Centralized manner
  Control whole of the Network in a Centralized manner
That’s exactly what we want:
SDN will provide us with the global knowledge of the network

## Slide 8: SDN: Overview

## Slide 9: Main Design

## Slide 10: What are the Design Objectives?
Maximizing the average overall throughput of flows/Minimizing the average flow completion time
Satisfying the Max-Min Fairness
  flows’ BW

## Slide 11: What are the Constraints?
A SDN based scheme
  The granularity is Flow-level not packet-level
  Setting flows up should be done in a dynamic/on-demand manner {Reactive Flow Installation }
  The number of Demands/Flows is variable during time
  For any new flow, we need to identify and set up the best path

## Slide 12: Main Design Steps
Path Database Construction
  Constructing Pre-Defined paths for each (src, dst) pair
Path Selection
  Choosing a path out of the pre-constructed candidate set for any new incoming flow

## Slide 13: Path Database Construction
We use two modes of path database construction
  Shortest paths
    Dijkstra Algorithm
  K-Shortest Path
    Yen Algorithm

## Slide 14: Bandwidth-Aware Path Selection
A Global-Greedy algorithm
Determine all the available paths for the incoming flow
Find the bottleneck link of those paths
  After applying max-min fairness, the lowest allocated BW for flows (L-BW) is on the bottleneck link
Pick the path with highest L-BW for the incoming flow

## Slide 15: Bandwidth-Aware Path Selection
Inputs:
  : Source node of the given flow
  : Destination node of the given flow
  : Pre-constructed path database, which consists of an associative array that maps pairs to a pre-defined set of candidate paths.
  : Current number of flows running on link .
  : Capacity of link .
Output:
  : The selected best path that yields highest max-min bandwidth allocation.

## Slide 16: Bandwidth-Aware Path Selection
Procedure :
for in do:
for in do:
if do:
if do:
for in do:

## Slide 17: Simulation Setup
  Simulator
    NS2, OPNET, and other simulators are packet based
    We designed our own flow based simulator
  Traffic Models
    Three different models:
      Gravity
      Uniform Random
      Anti-Gravity
  Flow Size Dist.
    lognormal

## Slide 18: Simulation Setup
  Topology
    Spanish Backbone Network including 30 nodes

## Slide 19: Evaluation Results
Anti-gravity Traffic model

## Slide 20: Evaluation Results
Uniform Random Traffic model

## Slide 21: Evaluation Results
Gravity Traffic Model

## Slide 22: Evaluation Results
Effect of Path Database Construction Alg.

## Slide 23: Conclusion
Experiment results show that the proposed bandwidth-aware path selection strategy outperforms ECMP and Uniform Random using different traffic models