## Slide 1
Panacea: Adaptive Traffic Engineering for Resilient Networks with Reinforcement Learning in SDN
Minghao Ye and Chen-Yu Yen
ECE Department
{my1706, cyy310}@nyu.edu
ECE7363 Project Presentation

## Slide 2
Outline
Introduction and motivation
Project idea
Methodology
Evaluation Result
Conclusion and Future Works

## Slide 3
Traffic Engineering (TE) and SDN
Traffic Engineering (TE): An important network operation for Internet Service Providers (ISPs) to optimize their networks
  Methodology: controlling traffic distribution and configuring the routing
  Goal: network performance (e.g. load balancing) & resource utilization
  Metric: The utilization of the most congested link, delay, etc.
Software-Defined Networking (SDN) provides opportunities for fine-grained per-flow routing based on its global view of the network
  The control plane can generate and deploy deliberate routing policies for different flows at the SDN switches.

## Slide 4
Introduction to TE
TE reroutes flows periodically to achieve load balancing
  The traffic demands among the nodes are changing dynamically
The following information is needed for TE optimization
  Topology: connectivity & capacity of routers & links
  Traffic matrix (TM): traffic demands between nodes in the network
Abilene Network: The variation of total traffic demands
Topology
Traffic Matrix
The variation of traffic demands is much larger in commercial network

## Slide 5
TE for Resilient Networks
Resilience: The capability of a network to recovery from failure
  For example, single link failure
Protection vs. Restoration
  Protection
    Allocates spare resources (such as backup paths)
    Fast recovery, but low spare capacity efficiency
  Restoration
    Computes new network configurations on the fly
    Slow recovery, but high resource efficiency
How to handle single link failures?
  Reroute the flows on surviving links
  Use TE to re-optimize network performance

## Slide 6
Motivation
Tradition TE solutions often reroute many flows (source-destination flows) to minimize the maximum link utilization (MLU) when network state changes.
Potential problem: significant network disturbance and service disruption.
  Changing the path of a source-destination flow could temporarily affect many TCP flows’ normal operation. [1]
    Packets out-of-order may trigger duplicate ACKs
    Falsely signal network congestion to the senders and reduce sending rate
    Increase the flow’s completion time and degrade users’ QoE
  How to mitigate the network disturbance with performance guarantee when there is a link failure?
[1] Carpa, Radu, et al. "Evaluating the impact of SDN-induced frequent route changes on TCP flows." 2017 13th International Conference on Network
and Service Management (CNSM).

## Slide 7
Insight
Our solution: Forward majority of traffic flows using Equal-Cost Multi-Path (ECMP) and only selectively rerouting a few critical flows using SDN to balance the link utilization.
We formulate the problem as a flow rerouting problem with 2 subproblems:
  Identify the critical flows from TM and topology
  Reroute the identified critical flows with different split ratios
The 2nd one is easy to solve by formulating it as a Linear Programming (LP) optimization problem once the critical flows are identified
The key problem is how to select the critical flows
  If we want to find 10 critical flows among 100 flows, the solution space has combinations!

## Slide 8
Panacea
Therefore, we propose Panacea: a Reinforcement Learning (RL)-based TE solution which can adapt to different failure situations in resilient networks
  Take the network topology and TM as an input
  Use RL to identify critical flows under different failure situations
  Formulate a LP problem to reroute the critical flows with SDN
Panacea can be trained to learn a selection policy over a rich variety of failure situations and historical TMs collected by the SDN controller
  The selection policy maps the topology and TM to the critical flow selection
The SDN controller installs and updates flow entries at the SDN switches to reroute the critical flows based on LP solution

## Slide 9
Workflow of Panacea
Panacea
1. Collect TM and current topology
2. Select Critical Flows
3. LP calculate split ratio
4. Deploy

## Slide 10
An agent receives observation from the environment, execute an action to the environment, and receive a reward signal as the feedback
Objective: find a policy that maximize the expected reward (, maximizing the network performance over various TMs)
A policy: An agent’s behavior. It is a map from state to action
What is reinforcement learning?

## Slide 11
Input/ State space: An RL agent take state
  is a traffic matrix at time , is the link status at time
Action space: The action is defined as {1, 2, … N*(N-1)} since there are totally N*(N-1) flows in the network, where N is the number of nodes
Given a state , the agent would sample K different actions as critical flows according to the probability of each action
Then, Panacea reroutes these critical flows and obtains the maximum link utilization by solving the rerouting optimization problem using LP
Reward: where is the maximum link utilization in the network. The smaller , the better performance and thus higher reward
RL Formulation

## Slide 12
Policy Network Architecture
N * (N-1) outputs
Each one corresponds to one of the flows
Softmax function for generating the probabilities for all actions
Training: Sample K actions according to the probability of each action
Evaluation (After training is done): Choose K actions with highest probabilities
Transformer
Encoder
MLP
Softmax
Selected flows
0 | 1 | 1
1 | 0 | 1
1 | 0 | 0
Link
Status
0 | 2.2 | 3.6
3.2 | 0 | 6.8
6.3 | 8.9 | 0
Traffic
Matrix
Sample each action according to
Learn the feature representations by
self-attention
(Attention is all you need!)

## Slide 13
Learn a Critical Flow Selection Algorithm
Advantage for variance reduction
This term can improve exploration by
discouraging premature convergence to suboptimal deterministic policies
Entropy factor set to 0.1
H is the entropy (the probability distribution over actions)
Sum over K actions
We train the agent using policy gradient (Actor-Critic method)
Maximize the reward using gradient ascend

## Slide 14
Training Panacea
We spawn 20 actor agents in parallel to speed up the training process
  Each actor agent is configured to experience a different set of TMs
  The central agent collects the experience tuples (state, action, reward) from actor agents and aggregates them to train the policy neural network
  The updated parameters are then sent back to the actor agents
Suppose there are 200 TMs in the training set. Each cycle is one iteration:
Central Agent
……
20 Actor Agents
Central Agent
……
20 Actor Agents
Each actor experience a different set of 200/20 = 10 TMs
Collect the experiences
Send back the updated parameters
Iteration 1, 2, 3…

## Slide 15
Rerouting Critical Flows
After selecting critical flows, we need to reroute them to achieve load balancing
The optimal multipath routing solution can be derived from LP for all critical flows.
The remaining flows running ECMP are regarded as background traffic.
Here are some notations:

## Slide 16
LP Formulation
Link load on link (i, j)
link capacity utilization constraint
flow conservation constraint
for critical flows
Split ratio constraint
Minimize MLU
Avoid unnecessary long paths
Background traffic
on link (i, j)

## Slide 17
Topologies
Panacea is tested on a real-world network topology
  Abilene Network: 12 nodes, 30 directed links, 12 x 11 = 132 flows
The real traces are publicly available
  Abilene TMs are measured every 5 minutes
  Training set: 288 TMs in Mar. 1st 2004
  Testing set: 288 TMs in Mar. 2nd 2004
Note: There are 2 routers in Atlanta

## Slide 18
Rule-based Heuristics
2 rule-based heuristics are also evaluated for comparison
Top-K: Selects the K largest flows from a given TM in terms of demand volume.
  Assumption: Flows with larger traffic volumes would have a dominate impact to network performance.
Top-K Critical: Selects the K largest flows from the most congested links.
  Assumption: Flows traversing the most congested links would have a dominate impact to network performance.

## Slide 19
Evaluation Scheme
All of the approaches: Panacea, Top-K, Top-K Critical and ECMP are compared to the performance of optimal explicit routing for all flows
Performance Ratio:
  : MLU achieved by an optimal explicit routing for all flows
  : MLU achieved by Panacea. It can be replaced by the MLU of other approaches to evaluate their performance ratio
means the performance is as good as optimal solution
The higher , the better performance is achieved

## Slide 20
Optimal Explicit Routing for All Flows
Given a network with a traffic demand matrix , the objective is to obtain the best explicit routing ratios to minimize the MLU in the network
This routing problem can be formulated as an optimization to obtain :

## Slide 21
Evaluation Results
Panacea can achieve near-optimal performance by rerouting only about 10% of all flows
Adapt to different failure situations and outperform the heuristics
Chart: Average Performance Ratio
| No failure | Failure 1 | Failure 2 | Failure 3 | Failure 4 | Failure 5 | Failure 6 | Failure 7 | Failure 8
Panacea | 0.9735 | 0.9966 | 0.9333 | 0.9959 | 0.9603 | 0.9684 | 0.9999 | 0.9698 | 0.9735
Top-K Critical | 0.9242 | 0.9863 | 0.881 | 0.9975 | 0.4315 | 0.513 | 0.9999 | 0.9292 | 0.9241
Top-K | 0.8253 | 0.9532 | 0.7932 | 0.9989 | 0.5564 | 0.4255 | 0.9998 | 0.8418 | 0.8253
ECMP | 0.6517 | 0.8663 | 0.6723 | 0.9885 | 0.4247 | 0.4068 | 0.9897 | 0.654 | 0.6517

## Slide 22
Evaluation Results

## Slide 23
Future Works
Increase the size of training set
  For example, use 2016 TMs in one week
Test our scheme on other failure scenarios
  Is it possible to extend our solutions to multiple link failures?
Use a larger network to test the scalability
  GEANT network (real traces): 23 nodes, 74 links
  Other ROCKETFUEL Topologies (synthesized TM): Ebone, Sprintlink, Tiscali…
GEANT
Ebone

## Slide 24
Conclusion
With an objective of mitigating network disturbance and improving network performance in resilient networks, we propose Panacea, an RL-based adaptive TE solution.
Panacea selects critical flows for each given traffic matrix under different failure situations and reroutes them to balance link utilization of the network by solving a rerouting optimization problem.
Extensive evaluations show that Panacea works well for different link failures and outperforms the best heuristic scheme by an average of 45.54% in the extreme case.
In addition, Panacea generalizes well to traffic matrices for which it was not explicitly trained.